# Dataflow in subdetectors

This document describes the dataflow between controllable electronics components of the subdetectors. This dataflow should be used as a basis for the schema of the configuration database.

Should we also describe: length, type and amount of cables?

Crate layout and connections between boards?

## Calorimeters

The cabling, positions and connections between boards and crates is described in note LHCb 2003-121.

#### Configuration of the FE board

The Calorimeter FE board is described in LHCb 2003-036.

Controllable items are:

- Low frequency noise suppressor method (subtraction of smallest of 2 previous measurements (default, “oldsubmod”) or estimate the pedestal as the lowest of previous plus a constant (to be set, “thresh”), and the previous)

- Allow no subtraction at all for testing (“sub zero”)

- Use a normal clock (default) or an inverted clock (channel per channel), “clkinvsel”

- Set the gain parameter for a channel to zero to allow it to be ignored by the trigger (for problematic channels)

- Choice of ADC or test pattern

- Choice of type of test:

  - Load the test patterns via I2C in the 3 “free” memory blocks of the AX250 to simulate the output of 4 ADC’s

  - Test charge at input of amplifiers

Need to understand the role of the CROC card.

Muon system

### Cabling and crates

FE boards on detector

Intermediate, Service and ODE boards beside detector (18 crates)

Pile-Up system

## L0DU

L1 and HLT

## VELO

## RICH1 & RICH2

### Cabling and crates

L0 electronics on detector

L1 boards in 4 crates

Total 4 racks, one crate per rack

Silicon Tracker, Inner Tracker

# Text boxes

FE chips

(16 per sensor)

Repeater board (5 per hybrid)

Digitizer board (input from 4 repeater boards)

Sensors (100)

7 SPECS slave boards to 100 repeater boards

Power supply

SPECS master (1)

TFC

L1-trigger farm

DAQ

CC-PC

L0 trigger

TTC

ECS

FE boards (MEP via Gbit Ethernet plugin cards), 126 L1, 323 HLT

Multiplexing switch (L1: 64, 2 links in, 1 out)

Readout switch

Subfarm controller (94)

Distributing switch

CPU (21 per farm)

L1 decision sorter

TFC

ECS

TELL1

L0 data

Multiplexing switch (HLT:  29, 11 links in, 1 out)

L0 DU board

L0 input from subdetectors (20 words)

Readout supervisor (1 word)

ECS

L1

HLT

Hybrids (4)

256 links each

1024 signals

Repeater board

Multiplexer boards (4)

Vertex finder boards (4)

Output board (1)

Tell1

L0DU

Physical channels (120k)

1248 optical links

ODE boards (148) 192 channels in, 12 links out

25920 LVDS links

Processing boards (60), 4 processing units each, 24 channels in, plus channels from neighbors

L1

ECS

FE boards (7632), 2 ASD’s, 8 channels per ASD, 16 in 8 out

Intermediate boards (152) (to generate logical channels)

Muon selection boards (12)

Controller boards (4)

L0DU

ECS

2 PCs, 4 CAN bus branches/PC, 21 ELMB CAN nodes/branch, 1 node per SB

Service boards  (144) low voltage to FE boards, synchronization signal

ECS

4 PCs, 6 CAN bus branches/PC, 24 ELMB CAN nodes/branch, 4 nodes per SB

write registers in DIALOG chip

power supply to FE boards

SPD (5984 cells)

PS (5984 cells)

Ecal (5984 cells)

Hcal (1468 cells)

4 crates (64 FE cards), 8x4 cells/card

14 crates (224 FE cards), 8x4 cells/card

28 validation cards (connected to 8 ECAL, 4 HCAL cards)

8 crates (128 FE cards), 8x8 cells/card

16 SPD sum cards

Selection crate (1 board for SPD, 3 for ECAL, 3 for HCAL)

28 inputs

L0DU

Tell1

SPD Very FE boards

PS Very FE boards

CROC

Pairs of HPD pixel chips (84 resp 131), 1024 channels per chip

Level-0 adapter board (84 resp 136, 5 single connections)

ECS (pixel chip configurations – shaping current, bias currents, discriminator values, masking, output multiplex grouping, pixel grouping, running mode, calibration values, via JTAG)

Level-1 readout boards (Tell1 ?, 21 resp 33)

ECS

RU supervisor (L0, L1 monitor, TTC driver)

DAQ

Service box

3 Beetle chips per hybrid (1 for each ladder)

Tell 1 board, 8 readout sectors in

DAQ

VCSEL transmitter

TFC

ECS slave (SPECS)

ECS master

I2C to GOL chips, Beetle FE chips, temperature monitors in FE box

GOL chip

4 FADC channels for 28 ladders

TFC

ECS