# Chapter 7 Implementation of the object layer

This chapter describes the object layer which consists of a set of autonomic tools implemented to interact with the CIC DB. The first section presents the two Perl scripts which are used to generate config files for the DHCP and DNS servers.

The second part explains the implementation details of the CIC library, namely its structure and its features. The third part describes the implementation of the two bindings with the issues. Finally the last part gives an overview of the PVSS library built for recipes.

## 7.1 Use of Perl scripts to generate config files

### 7.1.1 DHCP config file

This section describes how the dhcp config file can be generated using the connectivity information stored in the CIC DB. This method will be used to configure the network control interface of PCs in the farm, TELL1 boards and readout supervisors only. The IP addresses for the data interface will be attributed differently.

#### 7.1.1.1 Methodology

To create the dhcp config file, we use the following method [1]:

- Get the host nodes by generating the destination table of the given dhcp server name. Using the destination table (especially the portid of the last node) as described in 3.1.1, one can retrieve the PORT PROPERTIES, HW PORT PRORPERTIES and IPINFO tables, containing network information (MAC, IP and subnet addresses).

- Get the boot images. The boot image information is usually linked to the device type (CPU architecture, kernel version for instance). In most cases, all the farm nodes, TELL1 boards (per subsystem) and readout supervisors have the same boot image. However it may occur that a host has its specific boot image. To get the right boot image, we perform the 2 following steps:

  - Step 1: look if the given host name has a specific boot image in the DEVICE_BOOTING_TABLE in the CIC DB. If we find an entry corresponding to this node, we select it. If not, go to step 2.

  - Step 2: attribute it the boot image associated with the node’s devicetype. We get it from DEVICETYPE_BOOTING_TABLE.

- Getting the subnet ID. In the CIC DB, the subnet mask is stored instead of the subnet ID. However, one can compute the subnet ID given the subnet mask and the IP address.

For example:

IP address: 137.192.25.15 and Subnet Mask: 255.255.255.0

- Convert the IP address and the Subnet Mask to binary formats:

IP address:        100001001.11000000.00011001.00001111

Subnet Mask:     11111111. 11111111.11111111.000000000

We consider these two numbers as 2 vectors (32x1).

- Perform a point wise multiplication of the 2 vectors.

The subnet ID is then equal to 100001001.11000000.00011001.00000000

- Convert it to decimal format : 137.192.25.0

Group the hosts by subnet IDs as follows:

subnet 137.192.25.0 netmask 255.255.255.0 {

group {

host pctest32 {

hardware ethernet 00:00:A2:11:25:B4;

fixed-address 137.192.25.15;

filename “lynx_boot_23.nbi”;

}

host { ... }

}

subnet ...

At this stage, we have all the necessary information to build the dhcp config file. The next subsection will focus on the implementation.

#### 7.1.1.2 Generating and formatting the dhcp config file

Figure 1. Implementation principles.

Figure 1 describes how the DHCP config file has been generated.

It is based on a Perl script. Perl is one of the most used languages for writing Linux scripts. Perl also includes a lot of packages (XSLT, DBI, etc…) and is very convenient for string manipulation. Any time there is a change in the configuration of the network, the following steps should be carried out:

- The generic options are put in the “dhcp_options.xml” file provided with the application. There should one option per line. Referring to Figure 1, the generic options are written in red.

- Execute the Perl script, with the dhcp server name as input argument. It is case-sensitive. The Perl script performs three steps.

  - It obtains the network information (IP and MAC addresses, subnet_mask and boot image) from the CIC DB using Oracle XML[2] features such as “xmlelement”

  - It writes the results in the XML file “dhcp_file.xml”. The previously defined generic options are printed at the beginning of “dhcp_file.xml”. The result of the query is encapsulated in XML tags. The results are ordered by subnet ID.

  - It generates the dhcp config file using XSLT. XSLT is used to convert the XML file obtained into a dhcp config file. To do so, there is an XSL file which reads the XML file. It converts the XML tags into words which are understandable by a dhcp server.

For instance, the XML tag <ethernet_add> is converted into hardware ethernet, <ipname> to host, etc.

The output of these operations is the dhcpd.conf. All the files created and used are located in the same directory. The dhcpd.conf is copied in /etc/... manually by the network administrator. It is for security reasons. The whole Perl script can be found in Appendix C.

#### 7.1.1.3 Excluding nodes

If for any reason, a host needs to be excluded from configuration by a given dhcp server, it can be disabled by setting FUNCTIONAL_DEVICES.nodeused to 0. This function will exclude all the links affected by this change (CONNECTIVITY.lkused set to 0) and as a consequence, will update the DESTINATION_TABLE.pathused to 0 if one link has been disabled in a path.

When a host is disabled in the table, rerun the Perl script.

Then once this step is performed, include the hosts back again as the host has been disabled for generating a correct DHCP config file for a given DHCP server.

The following example illustrates the previous concept.

Figure 2. Example of a topology where it is mandatory to exclude nodes.

Assume a connectivity schema as in Figure 2. There are two DHCP servers, DHCP server 1 and DHCP server 2. The DHCP server 1 configures nodes from node_1_1 to node_1_32 and DHCP server 2 configures nodes from node_2_1 to node_2_32.

Both DHCP servers 1 and 2 could configure all the nodes. Therefore the destination table of DHCP server 1 is the same as that of DHCP server 2. It will contain all the host nodes, i.e. from node_1_1 to node_1_32 and from node_2_1 to node_2_32.  However the destination table for both DHCP servers 1 and 2 contains too many reachable hosts. Consequently the generated dhcp config file may be wrong depending on the network policy. So it is important to provide a solution if this case occurs. Then it will be up to the network administrator to decide what to do.

This problem can be solved by disabling hosts. The destination table of DHCP server 1 should contain only hosts from node_1_1 to node_1_32. Hosts from node_2_1 to node_2_32 must be excluded. When they have been excluded the Perl script should be executed to generate the dhcp config file for DHCP server 1. Then the excluded nodes must be included back so that the dhcp config file for DHCP server 2 can be generated. An example of C code is in Appendix D. It shows how this case can be handled.

In the same way, links can be disabled by updating CONNECTIVITY.lkused column.

In the previous example, another way to do could have been to exclude the link respectively between switch A and switch B (switch A and C) to generate the dhcp config file for DHCP server 2 (resp. DHCP server 1).

#### 7.1.1.4 Including nodes

The DAQ farm will grow over time as more PCs will be added. How this method will be affected by the arrival of new PCs or new TELL1 boards?

The impact is rather slight as the new devices and their connectivity only have to be added to the CIC DB.

The use of autonomics principles is reflected through 7.1.1.3 Excluding nodes and 7.1.1.4 Including nodes. The human intervention is reduced as it does not need to apply changes in the destination tables.

### 7.1.2 DNS files

The DNS provides the correspondence between IP address and IP name. We have tried to adopt a similar approach as for the DHCP config file. The information which needs to be predefined is the name of the domain, the name of the authoritative DNS server and the maximal number of times that a DNS config file can be recreated in one day. They are pretty static so they are saved as global variables.

To create the DNS files, we have split the code into 2 parts, one part which creates the forwarding file (given an IP name, retrieve the IP address) and the reverse file (given an IP address, get the IP name).  The whole Perl script can be found in Appendix D.

#### 7.1.2.1 Outline of creating the DNS forwarding file

This subsection describes how the DNS forwarding file is generated.

Figure 3. The principles of creating the DNS forwarding file.

Figure 3 describes the different steps performed to create the DNS forwarding file:

- Get the next serial. The serial identifies uniquely the dns file. Its value should be the same for the two set of files (forwarding and reversing as presented in Chapter 2). The two types of files start with some generic options showed below:

$TTL    86400

# name of the domain “.” is important             name of the DNS server

ecs.lhcb.       IN      SOA     dns01.ecs.lhcb.    root.localhost. (

#some generic options stored in the XML generic options file

200607130 ; serial

3h ; refresh

3600 ; retry

4w ; expire

3600 ; ttl

)

The serial is obtained by concatenating the current date (year/month/day) and a number. This number starts with 0 and is incremented whenever the DNS set of files has been re generated during a same day. This number should be less than P, maximum number to generate the DNS set of files, fixed by the network administrator. The default value (common value) is 9. If the serial is invalid, the program exits (and does not go through the reverse part).

- Use of XML in the SQL queries to get results formatted as followed:

<row><ipname>value</ipname><ipadd>value</ipadd><function>{NS,A,CNAME}</function></row>. Using regular expressions, the domain name is taken off from the ipname.

- Use of XSLT code to convert the XML file and the XML generic option file

#### 7.1.2.2 Outline of creating the DNS reversing file

This subsection describes how the DNS reversing file is generated.

Figure 4. Implementation guidelines of the creating the dns reversing file.

Figure 4 presents the implementation guidelines of creating the dns reversing file.

- Get the value of the serial parameter. It is equal to the one in the dns forwarding file and it is passed as an input parameter.

- Get the list of the IP addresses and IP names of all the equipment part of the control network with their subnet ID, using XML embedded in SQL. Store the results in an array.

- For each different subnetID, get the list of IP addresses and IP names of all the DNS servers (even if they are not in the given subnet) and format it for the subnet ID, like:

<row><ipadd>05.100.60.137.</ipadd>  <ipname>DAQ_CTRLPC_60_01.ecs.lhcb.</ipname> <function>NS</function> </row>

The IP addresses should be reverted. For instance, if the IP address is 123.23.56.45, it becomes 45.56.23.123. A dot should be put at the end to prevent from appending the subnetID at the end of IP address.

For the authoritative DNS server or also master DNS server (static variable in the script), it is formatted as follows:

<row><ipadd>137.56.in-addr.arpa.</ipadd> <ipname>DAQ_CTRLPC_10_01.ecs.lhcb.</ipname><function>NS</function></row>

In the previous example, 137.56.0.0 is the subnet ID. The “0” is taken off and replaced by “in-add.arpa”. Between <ipname> and </ipname>, there is the full name of the master DNS with the zone name (ecs.lhcb). The dot at the end is essential. If it is omitted, the zone name is appended to the name.

Add all the IP addresses and IP names which are in the given subnetID.

Using XSLT and the xml generic options (same as the previous one), convert the xml file into a reverse dns file for the given subnet ID.

The last step is iterated for all the subnet IDs. In the case of LHCb controls network, there are 4.

## 7.2 CIC_DB_lib, a C-library to query the CIC DB

### 7.2.1 Implementation guidelines

The CIC_DB_lib contains 157 functions and 58544 lines. It consists of 4 header files and 27 source files. The library has been compiled with MCV.Net v7.1 on Windows and gcc version 3.2.3 20030502 (Red Hat Linux 3.2.3-56) on Linux.

All the functions are documented and available on the Online web site [3].

#### 7.2.1.1 The CIC_DB_lib API

The purpose of the API is to allow a non DB expert user to interact with the CIC DB in a safe mode. To guarantee security, all the functions of the API are based on DML statements, i.e. the non DB-expert user is not allowed to drop a table as they are common to all the LHCb experiment.

To ensure that the library will provide all the information required by the different users of the CIC DB, the first step was to design the API.

The API is split into four parts (see Appendix F for the C interface):

- functions to query the content of the CIC DB (based on the SELECT statement);

- functions to populate the CIC DB(based on the INSERT statement);

- functions to update information stored in the CIC DB (based on the UPDATE statement);

- functions to delete information stored in the CIC DB (based on the DELETE statement);

The API has been improved and completed through discussions with the users of the CIC DB. As agreed, anybody should be able to have access to and to use any functions. There are no users’ privileges. All the SQL statements are hidden as the user is a non DB expert.

#### 7.2.1.2 Use of OCI

CIC_DB_lib is based on OCI (Oracle Call Interface) to access the CIC DB and on C as the programming language. The main advantage of the OCI interface is that it provides a lot of functions to interact with a database. It is faster than other interfaces as they are built over it (e.g. OCCI). It is more stable. It is recommended by Oracle for access to the database. So any type of statement can be done using OCI. However it is a quite complex interface.

To perform a SQL statement, the following common steps (quite similar to JDBC, ODBC or PERL DBI) are required:

- use of OCIHandleAlloc to allocate a handle.

- use of OCIStmtPrepare to prepare the query. A query can consists of a block of statements or a call to PL/SQL functions/procedures.

- use of OCIBindByName if there are some bind variables;

- use of OCIStmtExecute to execute the statement;

- use of OCIDefineByPos to define where to put the content of a column. To be used only for SELECT statement (not used in Perl DBI or ODBC);

- use of OCIStmtFetch2 to fetch the results of the statement (only for SELECT statement).

There is an example of a C code below. It returns the row of a given devicetype. Functions provided by OCI are in bold.

status =OCIHandleAlloc (ociEnv, (void**)&stmthp, OCI_HTYPE_STMT , 0, 0);

if(status!=OCI_SUCCESS)

{

rescode=ShowErrors (status, ociError, "OCIStmtHAndleStmt unsuccessful");

if(ociError!=0)

OCIReportError(ociError,appliName,ErrorMessage,1);

else

GetErrorMess(appliName,"NOT CONNECTED TO ANY DB",ErrorMessage,1);

return -1;

}

else

{

char selectdevtype[1000];

sprintf(selectdevtype,"select devicetype,devicetypeid,description,rgbcolor from %s where devicetype=:dtype ",DEVICETYPE_TABLE);

status=OCIStmtPrepare(stmthp, ociError, (text*) selectdevtype,(ub4) strlen(selectdevtype),(ub4) OCI_NTV_SYNTAX, (ub4) OCI_DEFAULT);

}

if(status!=OCI_SUCCESS )

{

if(rescode==0)

{

rescode=ShowErrors (status, ociError, "OCIStmtPrepare unsuccessful");

}

}

else

status=OCIBindByName(stmthp, &bnd1p, ociError,(text*)":dtype",-1,(dvoid*) devitype,strlen(devitype)+1, SQLT_STR, (dvoid *) 0,(ub2 *) 0, (ub2*) 0, (ub4) 0, (ub4 *) 0, OCI_DEFAULT);

if(status!=OCI_SUCCESS)

{

if(rescode==0)

{

rescode=ShowErrors (status, ociError, "OCIBindByPos unsuccessful");

}

}

else

status=OCIStmtExecute(ociHdbc, stmthp, ociError, 0, 0,(OCISnapshot *) 0, (OCISnapshot *) 0, OCI_DEFAULT);

if(status!=OCI_SUCCESS)

{

if(rescode==0)

{

rescode=ShowErrors (status, ociError, "OCIAttrGet2 unsuccessful");

}

}

else

{

status =OCIDefineByPos(stmthp, &def[0], ociError,1, (ub1 *) (devicetype_temp), devtypelen + 1,SQLT_STR, (dvoid *)&dtype_null,(ub2 *) 0,0, OCI_DEFAULT);

}

….

if(status!=OCI_SUCCESS)

{

if(rescode==0)

{

rescode=ShowErrors (status, ociError, "OCIDefineByPos4 unsuccessful");

}

}

else

status =OCIStmtFetch2(stmthp,ociError, 1, OCI_FETCH_NEXT,1, OCI_DEFAULT);

In parallel, there are other functions to tune statements such as the prefetch size memory by using OCIAttrSet (stmthp, OCI_HTYPE_STMT, &prefetch_rows, 0, OCI_ATTR_PREFETCH_ROWS, ociError). Prefetch_rows sets the number of rows which should be returned in one round trip. The typical value is between 1000 and 10000. It corresponds to the number of round trip (between the client and the DB server) and it should be set according to the network load average and the type of query. For instance, if a query will never return more than 1000 rows, there is no point in setting this parameter to 10,000.

The library can be used on Linux and Windows.

#### 7.2.1.3 Output format of a SELECT query

The functions based on SELECT statements are formatted as follows.

- The result of the SELECT is known to be one single row, then the return value is formatted as follows: |column_name: column_value (column_type) | …|, where | is a delimiter. It includes all the functions which return a row of a table given the primary key (deviceid, e.g.) or another candidate key (devicename). For example, GetFunctionalDeviceTypeRow returns the row of a given devicetype.

- The result of the SELECT returns a group of rows. The return value is either an array of int which correspond to the primary key of the table such as GetPortIDPerDevID which returns all the portids of a given deviceid. Or it can be a list of elements formatted as follows. Each row of the list is separated by ‘\0’ so that the mapping into vector of strings is easier (for PVSS and Python).

#### 7.2.1.4 Use of a memory cache for INSERT and UPDATE

For INSERT and UPDATE statements, a cache has been implemented to allow users to insert and update many rows in one go (bulk collect feature). It is well known that it is faster to insert multiple rows in one go than one row at the time.

To do so, a cache (using buffers) has been implemented to store all the rows which need to be inserted or updated. The user has to set the parameter last_rows to 1 to indicate that it is the last row which will be inserted or updated. So as long as this parameter is equal to 0, nothing will be inserted nor updated in the CIC DB. When this parameter is set to 1, all the rows are stored using OCIBindArrayOfStruct and sent to the CIC DB.

When inserting, deleting or updating many rows, it is very advisable to commit not too often but not after too many rows either. In the literature, a commit is advised to be performed every 10 000 rows. This value depends on the size of the rollback segment, a parameter set by the DBA. The more rows are updated without making a commit, the more space Oracle will need to save the content in case you rollback. On the opposite, if a commit is done frequently, it negatively affects the performance. A commit implies a lot of work such as synchronizing all the caches of all the current sessions. To make sure that a commit will not be performed after 20,000 rows or more, inserts or updates in the CIC DB are forced if the cache contains 10,000 rows, even if it is not the last row. So every 10,000 rows the cache is reinitialized. The database currently used is maintained by the Central Database Support. They advised me to commit every 10,000 rows. This value is set using #define MAX_ROWS 10,000, which is easy to update if there is any change in the rollback segment size.

#### 7.2.1.5 Querying paths between 2 devices

Another type of query is to get detailed paths between 2 devices or a device and a device type.

The first idea was to compute these paths using PL/SQL. However generating a destination table to get the detailed paths between 2 devices using PL/SQL is not the best method for two reasons:

- Getting the paths between 2 devices is very dynamic, in the sense that the name of two devices is not known in advance. So the DESTINATION_TABLE will contain too many rows and will be not easy to manage if we generate a destination table for each query “Get the paths between device A and device B”. Moreover nothing can be predefined contrary to generating the destination tables of the DCHP servers or the TFC switch.

- There is a performance issue. Getting paths between devices will be used to test links and to configure parameter values. Tests have been done between an implementation in C and PL/SQL code. C code was much faster as it has better memory and loop management.

Therefore algorithms to get detailed paths between device A and device B or device A and a device type have been implemented in C.

The main steps are:

- Load all the links which are part of the same subsystems as device A. If a path exists, there should be at least one common subsystem which includes device A and device B. In other words, a part of the CONNECTIVITY table is loaded in cache.

- Load the microscopic links of all the devices which are in the same subsystem as device A.

- Find all the paths starting from device A and ending at device B. A path cannot contain the same device twice and the pattern intermediate node-host node-intermediate node is rejected. It is the same as developed in PL/SQL package. Also there is a check that the combination (input, output) is valid. If data arriving at a given input can go out from the given output, then the path is kept, otherwise, it is rejected. The main advantage of this check is it is independent of the board connectivity. The same algorithm to get the macroscopic paths is applied to check that the given combination (input, output) is valid.

- Format and return the detailed paths if there are any.

- If not, we reverse the query. It means applying the previous steps by inverting device A and device B so that the results are independent of the direction of the query.

If whatever the query is, the subsystems are fixed, then there is no need to redo step 1. However, if new links have been added, a reload can be requested.

The query “get all paths through a device” is based on the same steps.

In any case, there is a timeout to avoid long computation of paths. It can happen if the user sets all the links to bidirectional and if there are a lot of devices with more than 100 ports.

#### 7.2.1.6 Error Handling

There is a handling for the following errors such as:

- Unsuccessful malloc if a memory allocation fails;

- NO_ROWS_SELECTED, if the result of the SELECT statement is empty;

- BUFFER_TOO_SMALL, if the size of the buffer to which the result should be copied;

- COULD NOT UPDATE ALL THE ROWS if some of the rows have not been updated. It is the case if the where condition is not satisfied. For instance,

Update functional_devices set nodeused=1 where devicename=’VELO_TLL1_23’. If VELO_TLL1_23 does not exist, this update will not work.

- COULD NOT INSERT ALL THE ROWS if some of the rows have not been inserted.

The Oracle errors explaining why a statement failed, such as a violation of a constraint or parent key not found are returned using the OCIError function. The complete Oracle error is returned in ErrMess, present in all functions of CIC_DB_lib. Besides the error which causes the failure, the name of function is also given.

### 7.2.2 Features of CIC_DB_lib

All these features have been checked to comply with the autonomic tools rules.

#### 7.2.2.1 Stability & security

To avoid any problem related to memory allocation, an application which uses CIC_DB_lib should allocate the memory. Indeed one of the common problems when implementing a library is to know which application should allocate the memory. We have agreed that CIC_DB_lib will not allocate the memory. However the application or the user will have to provide size of allocated buffers. For each function returning a list of devices, the user needs to specify the allocated size of the buffer in which the result should be put. If the size is too small, I put the required size in the variable which indicates the buffer size. If it is sufficient, I also put the real size needed here so that the application does not have to loop uselessly.

Example of use:

Int GetHistoryOfFunctionalDevice(char* functional_devicename,char* functionaldevice_history, int & len_history, char* min_date, char* max_date, char* ErrMess)

This function returns the history of a given device in functionaldevice_history. The application which calls this function has to put the allocated length of this parameter in len_history.

If the returned result can not be copied in functionaldevice_history, the size needed is put in len_history and I returned in ErrMess, BUFFER_TOO_SMALL.  If the allocated size is enough, I copy the result in functionaldevice_history and specify the length in len_history.

There was no security issue for the DB access as the CIC DB will be installed in a local network that is not accessible from the outside world. So there was no need for data encryption for instance. The only thing is that the user needs to connect the CIC DB by providing DB_name, login and password.

#### 7.2.2.2 Consistency

##### 7.2.2.2.1 Insert, update and delete information by block

Insert, delete and update functions have been implemented to ensure the consistency of the data in the CIC DB. The first thing is the block insertion (or update or deletion). It means that groups of data are inserted (or deleted or updated if required) together, using the same function. All these queries are part of the same transaction. Using this method, it avoids the user from calling several functions and it also prevents from forgetting to insert or update data.

Consider the following scenario. A user wants to insert a functional device. According to the table schema, inserting a functional device implies an insert in the HARDWARE_DEVICES, the FUNCTIONAL_DEVICES and the DEVICE_HISTORY tables. To allow efficient data consistency, the 3 inserts are done within the same SQL query. It consists of three consecutive SQL inserts. The main advantage is that if one of the inserts fails, the whole inserts fails. This is because of the use of foreign key constraints. Indeed, the first statement inserts into HARDWARE_DEVICES. Then the second inserts in FUNCTIONAL_DEVICES only if the first insert is successful. Finally the third ones inserts in DEVICE_HISTORY which can be done only if both previous inserts are successful.

The input parameters of InsertFunctionalDevices include all the table columns of HARDWARE_DEVICES and FUNCTIONAL_DEVICES.

Inserting by block is also used for port. If it is a DAQ device (i.e. it has an IP address), information will to be inserted in FUNCTIONAL_PORT_PROPERTIES, HARDWARE_PORT_PROPERTIES and IPINFO tables within the same SQL block.

The same concept has been applied for the UPDATE.

In the API, there are functions to delete links, ports, devices and device types. The user cannot delete a device if he has not deleted the ports of the device before.

When an insert, an update or delete affect the TFC or DAQ connectivity, a PL/SQL function part of routingtable_pck package updates the content of DESTINATIONTABLE, ROUTINGTABLE and PATH_LINES tables.

##### 7.2.2.2.2 Use of state diagrams for inventory

Inventory information requires a lot of checking to avoid inconsistency. To update the status of a device, there are three functions (and three for updating board component status):

ReplaceFunctionalDevice(char*devicename,char*

new_device_status,char*user_comments,char* status_datechange,char*serialnb_replacement,char*replace_date, char* ErrMess)

which allows the user to replace a functional device IN_USE by another hardware device (serialnb_replacement). The status of the hardware device which has been replaced must be specified (new_device_status). If the user sets serialnb_replacement to “none”, it means that the functional_device has status “NONE”.

SetToTestUseStatus(char* devicename, char* user_comments, char* status_datechange, char*serialnb_replacement, char* testboard_name, char*replace_date, char* ErrMess)

which allows replacing a functional device by another hardware device. The status of the hardware which was occupying the functional device is set to “TEST” and occupies a test board (testboard_name).

With these two functions any hardware device with status “IN_USE” can go to another status (TEST, EXT_TEST, DESTROYED or IN_REPAIR, SPARE).

UpdateHWDeviceStatus(char*devicename,char*new_device_status,char*new_location,char*user_comments,char* status_datechange,char*functional_devicename,char*ErrMess)

allows the user to set the status of a hardware device which does not have the status “IN_USE” to another status {EXT_TEST, DESTROYED or IN_REPAIR, SPARE, IN_USE}.

Using the following diagrams (see Figure 5, Figure 6, Figure 7, Figure 8, Figure 9) all the required checks can be made when updating the status of a device. Everything written in orange means it is an input parameter (provided by the user).

Figure 5. Replacing a hardware device.

Figure 6. Setting the status of a hardware device to “IN_USE”, with no replacement.

Figure 7. Changing the status of a hardware device from “IN_USE” to “TEST”, with replacement.

Figure 8. Changing the status of a hardware device from “IN_USE” to “TEST”, with no replacement.

Figure 9. Updating the status of a hardware device to “IN_USE”.

Each status change is inserted into the DEVICE_HISTORY table by CIC_DB_lib.

#### 7.2.2.3 Concurrency

Functions including insert or update statements have been tested in multi-user environment. In other words, different processes have executed the same function with different input parameters. This check was made to ensure that there was no blockage.

The tests have been performed on Windows using a C application which is based on the CreateProcess function. This function allows executing a function with specific command lines.

In fact, the different insert or update statements which correspond to a transaction were executed sequentially. During the tests, the “commit” or “rollback” statements were essential as it they prevent a SQL statement from blocking.

#### 7.2.2.4 Autonomics

CIC_DB_lib has been implemented to reduce the human intervention and to be self-adaptive in case of changes in the connectivity or the inventory.

This has been achieved by

- understanding the system (the architecture, the dataflow, what is allowed what is not)

- anticipating the different failures or changes which can happen (devices or links out of order, swapping two devices, etc.)

- providing the maximum of flexibility (possibility to test a part of a system by disabling/enabling some links or some devices, etc.)

### 7.2.3 Issues

The difficulties which occur during the implementation of the library were the following:

- Define a complete API. As the subsystems were built not at the same time, not all the functions have been implemented at the same time.

- Best way to send back the results of a retrieval query, especially regarding paths.

- Understanding OCI features.

## 7.3 Bindings

### 7.3.1 Implementation of the PVSS CIC_DB_lib

A PVSS extension of the CIC_DB_lib has been implemented to permit interactions with the CIC DB from PVSS.

It has been implemented using GEH. For each function of the CIC_DB_lib, a wrapper has been written based on TextVar and IntegarVar classes. There is one source file which contains all the wrappers. It has 10770 lines.

The code below shows an example of a PVSS wrapper for the function

DBConnexion(char* dbname,char* login,char* passwd,char* ErrorMess) :

/********************************************************************************/

/**

* Connect to the database taking 3 arguments and returning an integer value.

* @param server : name of the database.

* @param usr : user login.

* @param pwd : user password.

* @param errMess : return the ErrorMessage in case of failure (otherwise NO_ERRORS in + fct name)

* @return 0 if the disconnection is successful

*/

/*************************************************/

IntegerVar* PVSSDBConnexion(TextVar* server,TextVar* usr,TextVar* pwd,TextVar* errMess)

{

static IntegerVar c=0;

std::string dbname = server->getValue();

std::string login = usr->getValue();

std::string passwd = pwd->getValue();

int len_buffer=600;

char* ErrorMess=new char[len_buffer];

c=DBConnexion((char*)dbname.c_str(),(char*) login.c_str(),(char*) passwd.c_str(),ErrorMess);

errMess->setValue(ErrorMess);

delete [] ErrorMess;

return &c;

}

The extension exists both on Linux and Windows.

However I have encountered a compiler version problem. On Windows, Microsoft Visual 6.0 has to be used to compile it as the GEH has been built using this version.

Then on Linux, I have to use the compiler gcc version 2.96 20000731 (Red Hat Linux 7.3 2.96-113), an old version as the GEH has been compiled with this version. It was also not easy to get such a machine with this compiler version.

Finally, all the functions are documented and available on the Online web site [3].

### 7.3.2 Implementation of the Python CIC_DB_lib

There is also a Python binding. It is used by CDBVis, which will be explained in the next chapter. To interface it in Python, I used Boost. This is an open source project which allows any bindings from C++ to Python. It is very efficient especially to manage and convert C pointers into Python objects. Boost has been integrated in Gaudi which is an LHCb Computing framework. The main advantage to use Boost integrated in Gaudi is the maintenance of the module and the integration in the LHCb environment.

Here also I had to write a wrapper for all the functions of the CIC_DB_lib.

The result is a module (lib) cicDBpython which can be used in Linux and Windows. In a python script, the library can be used by doing “import (lib)cicDBpython”.

There was a need to implement two classes CICDB and CICDBEXCEPTION, to provide convenient error handling.

The attributes of CICDB are the connection parameters i.e. DB name, login and password. The methods of CICDB correspond to the functions implemented in the CIC_DB_lib.

The code below shows an example of a wrapper for the

DBConnexion(char* dbname,char* login,char* passwd,char* ErrorMess) :

int CICDB::PyDBConnexion()

{

int c=0;

int len_buffer=1000;

char* ErrorMess=new char[len_buffer];

string ErrorMess_copy;

c=DBConnexion((char*)_dbname.c_str(),(char*)_login.c_str(),(char*)_passwd.c_str(),ErrorMess);

if(c!=0)

{

ErrorMess_copy=ErrorMess;

delete [] ErrorMess;

throw CONFDBEXCEPTION(ErrorMess_copy);

}

delete [] ErrorMess;

return c;

}

Here I had two main problems:

- Handling of the in-out parameters as it does not exist in Python. Some of the results have been concatenated. For instance, the C function

int GetAllPathsPerDevice (  char *  systemnameList, char *  devname, int &  len_array, int *  lkid_list, int *  pathid_list, int *  link_pos_list, int  reload_connectivity, int  delete_connectivity, char *  ErrMessage )

becomes in Python,

vector< string > CICDB::PyGetAllPathsPerDevice (  string  systemname, string  devicename, int  reload_connectivity, int  delete_connectivity ).

The return value of this function is a vector of strings. Each row of this vector corresponds to the concatenation of pathid_list| link_pos_list|lkid_list|

- Compiler and Python version. It requires MCVNet v7.1 on Windows. It did not work with the previous version of Microsoft Visual because of boost. Moreover the module cicDBpython can work only with Python 2.3.4 because the Boost module (provided by GAUDI) has been compiled with this version of Python library.

Finally, all the functions are documented and available on the Online web site [3].

## 7.4 A PVSS library for recipes

The CERN PVSS Support has implemented a PVSS library to load and save recipes into/from PVSS. The documentation about the functions is included in the framework [4].

This library provides functions to load and save a recipe including versioning mechanism. It also includes functions to get the list of devices in a hierarchy, to get the list of available recipes (a device can be specified)

For instance the code below shows how to get the list of all the recipes stored in the CIC_DB, fwConfigurationDB_getRecipesInDB.

dyn_string exceptionInfo, recipeList;

fwConfigurationDB_getRecipesInDB(recipeList, exceptionInfo);

if (dynlen(exceptionInfo)) {fwExceptionHandling_display(exceptionInfo); return;}

RecipeSelector.items=recipeList;

## 7.5 Conclusions

In this chapter, the object layer has been described. Two Perl scripts have been used to generate the config file for both the DHCP and DNS servers. The one which creates the DHCP config file embeds PL/SQL function from the routingtable_pck to build the destination table.

CIC_DB_lib with its two bindings (PVSS and Python) enables non-DB expert to query, update and insert information about connectivity and inventory. Compiler version problem was the main issue when building these two extensions.

CIC_DB_lib has been built to be adaptive and smart, as any autonomic tools by reducing human intervention. To get and save information about recipes, the CERN PVSS Support has implemented a PVSS library which can be used in PVSS panels.

The next chapter explains how these libraries have been integrated in the GUI layer.

## References

[1] L.Abadie, Generating the DHCP config file using confDB, LHCb Internal Note, June 2006.

LHCb-2006-038

[2] ORACLE, Oracle® Database, SQL Reference, 10g Release 2, December 2005. B14200-02.

[3] CIC_DB_lib Documentation and its two extensions,

http://lhcb-online.web.cern.ch/lhcb-online/configurationdb/download_libraries.htm

[4] PVSS library for recipes,

http://itcobe.web.cern.ch/itcobe/Projects/Framework/Download/welcome.html