# Chapter 6 Automated creation of routing and destination tables using PL/SQL

This chapter describes the PL/SQL programs, part of the database layer. First, it gives some definitions about how I have modeled the nodes of the connectivity of a subsystem. The connectivity of the LHCb experiment is then represented as an ensemble of the connectivity of the different subsystems. Secondly, it describes the principles of the algorithm I have implemented to create the routing tables. It has been written as a PL/SQL package. Thirdly it presents the creation of the destination table, an extension to the algorithm that I used to handle the TFC partitioning and the automated creation of the dhcp config file. It is one of the key elements to build a set of autonomic tools.

Finally, it presents other PL/SQL programs I had implemented when the SQL statements were too complex and not suitable to be embedded.

## 6.1 Introduction

### 6.1.1 Problem

A routing table (for the DAQ switches) or a destination table (for the TFC switch or for the DHCP servers) provides information on how to reach possible destinations. To allow the creation of automatic routing or destination tables, we need to know if a device can be a destination, i.e. if it can receive packets. Typically a PC in the trigger farm will be a possible destination whereas a switch will not be a possible destination.

The query “Give all the paths (in a subsystem) which goes through a given device” is a problem too. As finding the longest path in a graph is a NP complete problem [1], finding all the paths is also a NP complete problem. So there is no algorithm which can solve this problem in a polynomial time, i.e. rapidly. Usually heuristic algorithms are used (tabu search [2] or genetic [3] algorithms for example). In our context, these types of algorithms could not be used as the output of the algorithm must be deterministic, i.e. same output at each execution of the algorithm.

We introduce a parameter M, the maximum path length, i.e. the maximum number of hops to put a limit on the research of paths. In the LHCb context, the topologies were such that it was sufficient to reduce the complexity of the problem. So the problem can be reformulated as finding all the paths whose length is less than M. M is set by the user or the application program.

The execution time depends on the topology of the graph, i.e. the number of vertices and the maximum path length found (the worst case is when it is a fully-connected graph because there are more paths).

The algorithm below has been described in [4].

### 6.1.2 Intermediate and host nodes and paths

A device can be either an intermediate or a host node. An intermediate node (switches, splitters, and L0 electronics) transfers the data without processing and manipulating it. A host node processes and modifies the data such as TELL1 boards and PCs. A host node has a more complex structure than an intermediate node. For example, the input data of a TELL1 board is generally a digital signal. The output data of a TELL1 board is zero-suppressed and formatted according to the MEP protocol. Figure 64 shows a slice of the DAQ connectivity. Orange boxes are host nodes (VELO_L1_21 and FARM0101 for instance are host nodes) and non-filled boxes are intermediate nodes such Force 10.

The FUNCTIONAL_DEVICES.node column, which is a flag, contains this information. The user must specify if the functional device is a host node (node=1) or an intermediate node (node=0). A host node is also the last device in the subsystem flow. So referring to Figure 64, VELO_L1_21 will have node set to 1 whereas Force 10 will have node set to 0.

Figure 64. Concept of host and intermediate nodes.

The concept of host and intermediate nodes is very useful to determine whether a device can be a destination. Only a host node can be a destination in a routing and a destination table.

In our context, a path can be defined as a sequence of nodes where there is one host node (the first node is not taken into account) and the last node is a host node. In other words, the pattern intermediate node - host node - intermediate node is not allowed in a path. Referring to Figure 64, [DS_SWITCH_01, FARM0101, DS_CTRLS_01] is not an allowed path as there is a host node between two intermediate nodes. A path can contain at most 2 host nodes. The position of a host node in a path is either the starting or terminal node.

The maximum number of hops (M) corresponds to the maximum number of nodes in a path. This parameter is a characteristic of the network.

A routing path is a special path which starts from an intermediate node (Force 10) and ends at a host node (FARM0101 for instance).

This concept of host and intermediate nodes allows splitting the huge connectivity of the whole LHCb experiment into smaller parts which corresponds to the subsystems. It has been applied for all the subsystems (of the detector and Online). Indeed there is no need to look for the RICH connectivity if a user or an application searches paths between a device A and a device B in the VELO subsystem.

### 6.1.3 Link and path weights

To compute and find the routing paths easier, we have introduced the concept of link and path weights.

The CONNECTIVITY.link_weight column represents the weight of a link noted W(L) and automatically set to (see Figure 65):

- 0 if the link is between 2 intermediate nodes

- 1 if the directed link is between a host node and an intermediate node

- 2 if the directed link is between an intermediate node and a host node.

- 3 if the link is between two host nodes (although not used here)

The path weight W(P) is defined as the sum of the link weights along the path. By using the definition of the routing path, we can derive the following theorem which will be used to find the subset of routing paths from paths.

A path P of length J is a routing path of length J

where W(L)i corresponds to the weight of the i-th link in the path P. Thus, a path of length J is a routing path of length J if and only if the all the weights of the links (so the J-1th links) are equal to 0 and the weight of the last link (the Jth link) is equal to 2. The proof is given in the Appendix A. Figure 66 shows an example of a routing path.

Figure 65. Link weight concept.

Figure 66. Example of a routing path.

## 6.2 Algorithm to generate routing tables

### 6.2.1 Routing tables (reminder)

A routing table consists of providing the following information:

- IP address of the destination;

- Port number to which the IP packet should forwarded;

- IP address of the interface of the next hop;

- Subnet mask of the next hop.

The concept of routing tables has been explained in detail, in Chapter 3, section 4.

### 6.2.2 Principles of the algorithm

Let’s denote L(node i, node j), the link between node i and node j, W(L) the weight of the link and S(node i, node j, node k,…., node t) a sequence of nodes between node i and node t. W(S) is the weight of the sequence (sum over the weight of the links which compose the sequence)

We give an overview of the algorithm which finds routing paths using the connectivity of the DAQ network. The input parameters are the name of the router and the parameter M (default value 10). The steps are as followed:

- Simplify the connectivity of the system by removing the port level. For instance if there is two links between device A and device B, we just consider it as one link between device A and device B. It is for efficiency reasons.

- Revert all the links which are bidirectional so that we really find all the paths. For instance if there is a bidirectional link between device A and device B. It is saved as one link starting from device A to device B and one link from device B to device A.

- Find all the links which starts from the given router and which have a link weight equal to 2. We then found all the routing paths of length 1.

- Group the links by per of two by making sure that it verifies the three conditions

  - the second node of the first link is equal to the first node of the second node (necessary condition to build a path);

  - the first node of the first link is not equal to the last node of the second link (to avoid cycles);

  - the weight of the first link is not equal to 2 (to verify the routing path condition where only the last link should have a weight equal to 2).

  - Compatibility of the link types between the two links to ensure a consistent path. If a link carries data traffic and another link carries controls traffic, the two links cannot be compatible. But if a link carries both controls and data traffics and another link carries only data traffic, then the two links are compatible and the type of this link pair is then data traffic only.

In other words, the pair of links (which is a sequence of 3 nodes) is valid if and only if S(node i, node j, node k)= L(node i, node j) and L(node j, node k) where node k ≠ node i and W(L(node i, node j))≠2.

- At each iteration, add a link L( node u, node v) to a sequence of nodes S(node i, node j, …, node t) already found if it verifies the following conditions:

  - The weight of the sequence is not equal to 2 otherwise the sequence is already a routing path so we don’t touch it.

  - node u= node t. The first node of the link should correspond to the last node of the sequence of the nodes. (otherwise there is no communication between them)

  - node v is not already in the sequence of nodes to prevent cycles.

  - The link type of L( node u, node v) should be compatible with the link type of the sequence of nodes.

If the node passes the conditions, it is added to the sequence of nodes and the weight of the sequence is updated and the type of the sequence too.

So at each iteration, the length of the sequence is increased by one. The loop stops when all the paths found are routing paths, i.e. all the weight of the paths are equal to 2 or the path length is greater than M.

- Each routing path is now completing with the port numbers.

- Then for each distinct destination found (last node in the routing path), select the shortest path found.

- Information about the IP and MAC addresses is performed dynamically (using the port number of the device) when loading the routing table of the given switch to make the updates of the routing tables easier.

### 6.2.3 Convention

Tables which are suffixed by “_TEMP” are temporary tables. For instance, there is PATH_LINES which is a real table and PATH_LINES_TEMP which is a temporary table with the same structure as PATH_LINES. These tables are not represented in Figure 67 for clarity purposes. An exception has been made for LINK_PAIRS and AGGREGATED_LINKS which are temporary tables, because we estimated that they are important tables. There are no constraints as we do not define constraints for temporary tables. Intermediate results are stored in temporary tables.

### 6.2.4 Initialization

The input parameters of the routing algorithm are the name of the switch (the one for which we want to generate the routing table) and M.

Figure 67.  Path modeling.

The algorithm to generate the routing table is based on the following steps:

- Create the AGGREGATED_LINKS table (a temporary table) which contains all the links between devices. If a link is bidirectional, we store the reverted link. The principles of this creation are shown in Figure 68. The port number concept is not considered.  For instance if the Force 10 router is connected via 10 links to a distribution switch. In the AGGREGATED_LINKS table, one link is considered between the Force 10 and a distribution switch. It is derived from the connectivity table (cf Figure 67). This step permits to reduce the number of links to be handled.

Figure 68. Generating the AGGREGATED_LINKS table using the CONNECTIVITY table.

- Create the LINK_PAIRS table (a temporary table) which contains all valid pairs of successive links (one node in common). For instance, the link between Force ten and distribution switch 1 and the link between distribution switch 1 and Farm node 1.

To create the LINK_PAIRS table, we perform a self-join of the AGGREGATED_LINKS table with the following constraints:

  - Link1 is defined by (Node_1, Node_2) and Link2 is defined by (Node_2, Node_3) (referring to Figure 67) where Node_2 corresponds both to Node_to of link1 and to Node_from of link2.

  - The link_weight of link1 must be equal to 0 because we want to find routing paths (i.e. it starts and ends from/at a switch and, as we are looking for pairs of links, we exclude the switch-host links).

- The PATH_LINES_TEMP table is initialized with the elements from the AGGREGATED_LINKS (to find path length equal to 1) and LINK_PAIRS table which have the switch given as input parameter as a starting node (Node_1 column).

We then have found paths which have a length equal to 1 or 2. These paths are inserted in the PATH_LINES_TEMP table. If the path length is equal to 1, then the path is inserted as a row into the PATH_LINES_TEMP table using the columns Node_1, Node_2. If the path length is equal to 2, then the path is inserted as a row into the PATH_LINES_TEMP table using the columns Node_1, Node_2, Node_3.

### 6.2.5 Body

This subsection explains how we find the routing paths.

We iterate over i which represents the path length.

At each iteration of i, a join between the LINK_PAIRS and the PATH_LINES_TEMP tables is executed. This means that a path P, with W(P)=0 (i.e. having not reached a host) is completed with an element from LINK_PAIRS whose  first link is equal to the last link of P.

If no such pair exists, the path P is removed. There may be more than one pair which satisfies the conditions. Thus if there are N possible pairs, these N possible pairs will be appended to P and there will be N new paths (i.e. N new rows in the PATH_LINES_TEMP).

At the end of iteration i, we have found all the paths of length i and inserted them in the PATH_LINES_TEMP table and we have filled the i +1 Node columns of PATH_LINES_TEMP table.

For each iteration i, the detailed description of the steps is as follows:

- In the PATH_LINES_TEMP table, select the paths P where W(P)=0. (The last column filled is Node_i).

- Find all the possible pairs of links where (Node_i-1, Node_i) is equal to (Node_1, Node_2) of LINK_PAIRS table and check that there is no cycle (i.e. a node appearing twice in the path).

- Insert these new valid paths in the PATH_LINES_TEMP table. So the Node_1 to Node_i+1 columns are filled in.

- Delete the old paths where W (P)=0 and Node_i+1=0.

- Increment i by 1.

- Stop the loop if i is greater than M or if all the paths are routing paths, i.e. all paths verify  W (P)>0.

- Go back to the port level for the first and last links and insert the portids of the network interface starting the path, ending the first link and ending the path into ROUTING_TABLE_TEMP. Finally, we resolve multiple paths to a given (destination, network interface) by setting the routingpathused column to 1 for the shortest routing path (required by the DAQ team).

- Insert the valid routing paths found in PATH_LINES_TEMP into PATH_LINES, in ROUTING_TABLE_TEMP into ROUTING_TABLE.

Commit to delete the content of the temporary tables, except the content of AGGREGATED_LINKS and LINK_PAIRS. They are kept as they can be reused for another switch if it is part of the same subsystem.

This algorithm has been tested against several network architectures including full mesh layouts (see Chapter 9).

Remark on step 6:

If the loop is stopped because of M, paths whose length is greater than M are not found. We trust the user or the application in setting a correct value of M.

### 6.2.6 Routing table

The PATH_LINES table contains all the routing paths of a switch in detail with the different hops. The pfromid0, ptoid0 and ptoid1 columns of ROUTING_TABLE respectively represent the portid of the network interface of the nodeid_start0, the portid of the network interface of the next hop and the portid of the destination network interface.

The port number to which the packet should be sent is retrieved using pfromid0. The IP and MAC addresses of the next hop are found using ptoid0 and the IP address of the destination is known using ptoid1.

The routing paths used to program the switch are stored in the ROUTING_TABLE table with routingpathused set to 1. It allows a better update and management of paths in case of a problem with a port or a device.

A join between the ROUTING_TABLE table, the FUNCTIONAL_PORT_PROPERTIES and IPINFO tables permits to get the IP address and the subnet mask. We do a join between the ROUTING_TABLE table and the FUNCTIONAL_PORT_PROPERTIES and HARDWARE_PORT_PROPERTIES tables to get the mac_address. To avoid many updates in case of a MAC address or an IP address changes, the two joins are performed on the fly, i.e. when the user asks for loading the routing tables.

All the routing tables, i.e. all the routing tables of the DAQ switches, are stored in ROUTING_TABLE (one table only).

### 6.2.7 PL/SQL package

All the steps which have been previously described have been included in a PL/SQL package, routingtable_pck (the interface is shown in Appendix B). The package body has 1797 lines of code.

PL/SQL is a proprietary (Oracle) language; the code is executed at the server-side. PL/SQL can be embedded in other languages such as JAVA, C, PERL, etc. A PL/SQL package is stored in its compiled form. The parsing of SQL queries is performed only at compiling time.

When a procedure of a package is called, first Oracle gets the package and loads it into memory if it is not already there. So performance is improved as parsing SQL queries can be quite time consuming depending on the complexity of the query.

By using PL/SQL one avoids overloading of the network by very long sequences of SQL queries. Also the maintenance of the routing tables is easier. Whenever there is a change in the CONNECTIVITY TABLE, ROUTING_TABLE and DESTINATION_TABLE related to DAQ or TFC system are recreated.

Generating a routing table is performed using 4 functions of routingtable_pck.

- The first function creates and filled the AGGREGATED_LINKS and LINK_PAIRS tables.

- The second function finds all the routing paths which start from the given devices using the logical view. These are stored in the PATH_LINE_TEMP table. STARTEND_TEMP is also filled with the two first and the two last nodes. It will be used to select the right port interfaces.

- The third function maps the start (the first link) and the end (last link) of the path with PORT_PROPERTIES.portid with all the checks (same link type, bidirectional link used, link used or not) and inserts them in ROUTING_TABLE_TEMP. One routing path is selected by (destination, network interface) among the valid paths, i.e. where no link is disabled or broken. Set routingpathused=1 to the selected routing paths.

- The fourth function deletes the old entry related to the given switch and inserts all the results in the tables PATH_LINES and ROUTING_TABLE.

### 6.2.8 Completeness of the algorithm

The routing algorithm finds all the paths less than M (less than 10 in the context of LHCb). The proof relies on the “join” operator reliability. Figure 69 illustrates the concept. If a valid path is not found with a length less than M, it means that during the join operation the code could not find a pairs of links which matches the current path. It means that this pair of links is missing. So it means that this pair of links is not in the LINK_PAIRS table which is the result of a self-join with constraints of the AGGREGATED LINKS TABLE. The join operator in SQL is known to be reliable. So if this pair of links is not in the table, it means that the pair of links fails to satisfy the constraints, which is in contradiction with the fact that is a valid path.

Figure 69. Concept of finding the paths. The path starting from Node 1 to Host Node i+2 is a routing path. The other path ending at Node i+2 is still not finished, we go on if the i+3<M.

## 6.3 Extensions of the routing table algorithm

### 6.3.1 Partitioning

#### 6.3.1.1 Destination table

In Chapter 2, section 2.3, partitioning has been handled using the destination of the TFC switch. A destination table of a device consists of the following columns (which are almost similar to ROUTING_TABLE):

- Deviceid of the node1 (which starts the path). This node corresponds to the deviceid of the functional device for which the destination table is generated. For instance, if we generate the destination table of the TFC switch, the value of this column corresponds to the deviceid of the TFC switch.

- Portid of the node1 (from which the link starts). This column permits retrieving information about the port which starts the path. In the case of the TFC switch, it corresponds to the port IDs of the output ports.

- Portid of the last node (at which the link ends) allows retrieving information about the port which ends the path. In the case of the TFC switch, it corresponds to the port IDs of the input ports of the destination devices, i.e. the TELL1 boards.

- Deviceid of the destination devices.

- System name which corresponds to the list of subsystems of which the destination device is part.

- Pathused which indicates if the path is functional (1) or not (0). For instance if a device is broken and not replaced or if a device needs to be excluded for debugging reasons, for instance, all the paths which go through that device are disabled, i.e. pathused=0.

All the destination tables which are generated are stored in DESTINATION_TABLE.

#### 6.3.1.2 Algorithm principles

The routing algorithm has been adapted to generate a destination table as the concept is similar. The main difference is that the destination table can be generated for a host node.  So the computation of the path weight is slightly different. However the algorithm principles are the same in both cases.

- The first step is to determine whether the destination table is for a host or intermediate node.

- If it is a host node, the path weight should be equal to 3 =(1 +2 )

- If it is an intermediate node, the path weight should be equal to 2 = (0+2). It is the same as for the routing tables.

Also all the paths are inserted. In other words, it is possible to have several paths which start from the same pair (deviceid of the first node, portid) unlike the routing tables.

The functions which are used to generate the destination tables are also included in the routingtable_pck PL/SQL package.

#### 6.3.1.3 Example of the TFC switch

Figure 11, in Chapter 1, shows the connectivity of the TFC. The readout supervisors (ODIN) and the TELL1 boards are respectively the sources and destinations. Thus they are host nodes, the other devices are intermediate nodes.

All the links in the TFC system are unidirectional. The TFC switch can only send information to TELL1 boards, which are the only possible destinations in that case.

A readout supervisor can not be a destination as it is a source (it sends information but does not receive any data via the TFC switch). The destination table of the TFC switch will contain around 350 distinct destinations (equal to the number of TELL1 boards).

The TFC system needs to know the output ports of the TFC switch which drive the subsystems in the partition to configure the switch.

Consider the following example. An extract of the TFC destination table is shown in Table 16.

| TFC output port nb | Port way | Port type | Destination device name | System ID of the destination |
| --- | --- | --- | --- | --- |
| 0 | 2 | None | VELO_L1FE_04_00 | 1155 |
| 0 | 2 | None | VELO_L1FE_04_01 | 1155 |
| 1 | 2 | None | VELO_L1FE_07_04 | 1365 |
| 1 | 2 | None | VELO_L1FE_07_04 | 1365 |
| 2 | 2 | None | RICH1_L1FE_09_08 | 4845 |
| 2 | 2 | None | RICH1_L1FE_08_02 | 4845 |
| 3 | 2 | None | RICH2_L1FE_00_01 | 5865 |
| 3 | 2 | None | RICH2_L1FE_00_02 | 5865 |
| 10 | 2 | None | L0MUON_L1FE_00_03 | 98355 |
| 10 | 2 | None | L0MUON_L1FE_00_01 | 98355 |
| 10 | 2 | None | L0MUON_L1FE_00_02 | 98355 |
| 4 | 2 | None | IT_L1FE_09_00 | 26445 |
| 4 | 2 | None | IT_L1FE_09_00 | 26445 |
| 4 | 2 | None | IT_L1FE_09_00 | 26445 |
| 5 | 2 | None | TT_L1FE_03_01 | 28905 |
| 5 | 2 | None | TT_L1FE_03_01 | 28905 |
| 5 | 2 | None | TT_L1FE_03_01 | 28905 |
| 6 | 2 | None | OT_L1FE_00_12 | 13485 |
| 6 | 2 | None | OT_L1FE_00_11 | 13485 |
| 6 | 2 | None | OT_L1FE_00_10 | 13485 |
| 7 | 2 | None | OT_L1FE_02_05 | 16095 |
| 7 | 2 | None | OT_L1FE_01_21 | 16095 |
| 7 | 2 | None | OT_L1FE_01_09 | 16095 |
| 8 | 2 | None | PRS_L1FE_03_00 | 915 |
| 8 | 2 | None | PRS_L1FE_01_00 | 915 |
| 8 | 2 | None | ECAL_L1FE_02_00 | 795 |
| 9 | 2 | None | ECAL_L1FE_04_00 | 795 |
| 9 | 2 | None | ECAL_L1FE_03_00 | 795 |
| 11 | 2 | None | HCAL_L1FE_01_01 | 885 |
| 11 | 2 | None | HCAL_L1FE_01_00 | 885 |
| 12 | 2 | None | MUON_L1FE_01_00 | 71355 |
| 12 | 2 | None | MUON_L1FE_01_00 | 71355 |
| 13 | 2 | None | MUON_L1FE_01_00 | 73365 |
| 13 | 2 | None | MUON_L1FE_07_00 | 73365 |
| 13 | 2 | None | MUON_L1FE_07_00 | 73365 |
| 14 | 2 | None | L0CALO_L1FE_00_00 | 105465 |
| 14 | 2 | None | L0CALO _L1FE_00_01 | 105465 |
| 14 | 2 | None | L0CALO _L1FE_00_02 | 105465 |
| 15 | 2 | None | L0DU _L1FE_00_01 | 119685 |
| 15 | 2 | None | L0DU _L1FE_00_02 | 119685 |
| 15 | 2 | None | L0DU _L1FE_00_03 | 119685 |

Table 16. Extract of the TFC destination table.

For example, for a partition consisting of {VELO, RICH, OT_A}, the SQL query:

select distinct port nb from DESTINATION_TABLE r, FUNCTIONAL_DEVICES t, SUBSYSTEM_LIST l where r.nodeid_start=t.deviceid and t.devicename=’TFC_SWITCH’ and l.system_name=’VELO’ and mod (r.systemid, l.systemid) =0.

will only select the destination devices belonging to these subsystems. The result of the query is 0 and 1.

The same query is performed for RICH and OT_A so that each subsystem can be properly associated with 1 or two output ports of the TFC switch.

The selected destinations with their associated output port(s) are written in bold in Table 16.

### 6.3.2 Generating the DCHP config file

The destination table is generated for the DHCP server to get all the host nodes which can get their IP address from the given DHCP server.

It has been integrated in a Perl script which is described in the next chapter.

## 6.4 Other PL/SQL programs

Besides the PL/SQL package routingtable_pck, there are other PL/SQL programs which have been implemented to avoid embedding long sequences of SQL queries (essentially updates and insertions).

- UpdateDeviceHistory : a PL/SQL function

- UpdateBoardComponent: a PL/SQL function which updates the status of the microscopic devices (components of the board) according to the change of the status of the motherboard. (the status should be different from TEST)

- SwapTwoDevices: a PL/SQL function which swaps two devices and checks that this operation is allowed (for instance same number of ports connected and same device type).

- InsertSubsystem: A PL/SQL function which inserts a new subsystem and attributes it a systemID.

- ComposeFunctionID: a PL/SQL function which returns the function ID given a list of function names.

- DecomposeFunctionID: a PL/SQL function which returns the function names given a function ID.

- InsertIPaddress: a PL/SQL function which inserts an IP address. It is used when inserting a port of a device. There is a need to know if the IP address already exists or not. If not, it inserts it.

- UpdateIPaddress: a PL/SQL function which updates an IP address further to a mistype or a change. It performs the update for IPINFO, IPALIAS and PORT_PROPERTIES tables.

- TestUseBoardCpnt: a PL/SQL function which sets the status of the microscopic devices (components of the board) to TEST when the motherboard goes to TEST.

- InsertTestBoard: a PL/SQL procedure which inserts a test board. The name of a board test is automatically generated by the CIC DB.

- CreateTableSchema: a PL/SQL function which creates the CIC DB schema (tables, indexes and constraints).

- DropTableSchema: a PL/SQL function which drops the current CIC DB schema.

## 6.5 Conclusions

This chapter describes how routing and destination tables can be generated using the information stored in the CIC DB. The algorithm is based on two main concepts:

- Intermediate and host nodes to make the distinction between possible destinations for the routing table and also to put boundaries to the network of a subsystem

- Paths and path weights to compute the correct paths by avoiding cycles.

The algorithm implemented in PL/SQL is used mainly for fixed queries such as

- generating the routing tables of the DAQ switches,

- generating the destination table of the TFC switch for partitioning,

- generating the destination table of the DHCP servers to create the dhcp config file.

All the routing tables (DAQ switches) and destination tables (TFC switch and DHCP servers) are respectively in the ROUTING_TABLE and DESTINATION_TABLE. They are automatically updated.

It also describes the other PL/SQL codes which have been implemented when a query was too complex or implies too many checks. It was the case for some insertions and updates.

So the implementation of the database layer has been described over Chapter 5 and 6. The next chapter will focus on the object layer.

References

[1] M.R.Garey and D.S.Johnson, Computers and Intractability: A Guide to the Theory of NP-Completeness, 1990. W. H. Freeman & Co.   New York, NY, USA. 0716710455. 338 p.

[2] Gendreau M. An introduction to tabu search. In: Glover F, Kochenberger GA, editors. Handbook of metaheuristics. Boston, Dordrecht, London: Kluwer Academic Publishers; 2003. p. 37-54.

[3] Genetic Algorithm, http://en.wikipedia.org/wiki/Genetic_algorithm

[4] L.Abadie, Configuring the LHCb Redaout Network using a database, August 2006.

IEEE Transactions on Nuclear Science, June 2006, Vol. 53, number 3, Part I of three parts. 14th Conference on real time (RT 2005) Stockholm, Sweden, June 4-10, 2005. p995-1001.

# Footnotes

Temporary tables have no foreign key and no primary key. That is why LINK_PAIRS and AGGREGATED_LINKS seem disconnect from the schema. They are temporary tables as there is no need to keep their content.