## Slide 1: LHCb Operations in Run I:
Challenges and lessons learnt

## Slide 2: Operations
Operations Strategy
  2 people on shift (from day one)
    1 Shift Leader (and main operator)
    1 Data Quality Manager
    and small on-call team: ~10 people
  Integrated Control System
    Homogeneous User Interfaces to all areas:
      Data Acquisition (DAQ), Detector Control System (DCS), Trigger, High Level Trigger (HLT), etc.
  Full Automation
    For standard procedures and (known) error recovery

## Slide 3: Operations Scope
Detector Channels
Front End Electronics
Readout Boards
High Level Trigger (Farm)
Storage
Trigger
Experiment Control System
DAQ
Detector & General Infrastructure (Power, Gas, Cooling, etc.)
External Systems (LHC, Technical Services, Safety, etc.)
Timing
Monitoring
Offline Processing

## Slide 4: Operations Tools
Run Control Automation: The Autopilot
  Configures, Starts and Keeps the RUN going. Recovers:
  Sub-detector de-synch.
  Misbehaving farm nodes
  Etc.

## Slide 5: Operations Tools
Big Brother
Based on LHC state, controls:
  Voltages
  VELO Closure
  Run Control
Can sequence activities, ex.:
  End-of-fill Calibration
Confirmation requests and Information
  Voice Messages

## Slide 6
Selected Challenges…

## Slide 7: VELO Closing
Take data (DAQ)
3D Vertex Reconstruction (HLT Farm)
Calculate next VELO position (Monitoring Farm)
Move VELO (DCS)
Big Brother
Safety: Many criteria to respect
Procedure: Iterative “Feedback” loop

## Slide 8: VELO Closing
Manually operated in the beginning
Completely automated since 2011
  Takes ~4 minutes at start of fill
LHCb Efficiency breakdown 2012

## Slide 9: Luminosity Levelling
Allows running LHCb under stable optimum conditions
Constraints: Safety and Reliability
Lumi controller
LHCb Leveling GUI Configuration & Monitoring
LHCb readout system
LHCb
CERN data exchange protocol (TCP/IP)
LHCb Luminosity detectors
Instant Lumi Target Lumi Levelling Request Step Size
Levelling Enabled Levelling Active …
LHC Control System

## Slide 10: Luminosity Levelling
In operation since 2011
95 % of integrated luminosity recorded within 3% of desired luminosity
Thanks to the LHC experts and operators

## Slide 11: HLT Farm Usage
Farm Node
Farm Node
Resource Optimization -> Deferred HLT
  Idea: Buffer data to disk when HLT busy / Process in inter-fill gap
  Change of “paradigm”: A run can “last” days…
Standard HLT
Deferred HLT
Farm Node
Farm Node during Physics
Farm Node Inter-fill
1 MHz
5 KHz
70 KHz
HLT
HLT
HLT
EvtBuilder
EvtBuilder

## Slide 12: Deferred HLT
Major Success
  In place since 2012
  ~20% resource gain for HLT
    Better Trigger
  Cushion for central DAQ/Storage hiccups

## Slide 13: HLT Farm Usage
Resource Optimization -> Offline Processing
  Idea: Run standard Offline Simulation outside data taking periods
  Online Control System turns HLT Farm into Offline site
  In Operations since end 2012
Also a big Success:
  ~25K jobs simultaneously
  Largest LHCb producer

## Slide 14: Distributed Computing
Reconstruction
Storage (CASTOR)
Stripping
Analyses
From Online Full Stream 5 KHz
Reconstruction
Storage (CASTOR)
Calibration & Alignment
From Online Express Stream 5 Hz
Data Quality
Data Quality
Conditions DB
GRID
CERN
Running Fine
  126 sites in 20 countries
  2 Shifters (daytime only)
Running Jobs since 2012
CPU Usage since 2012
Generation

## Slide 15
Lessons Learnt…

## Slide 16: HLT Farm Usage in RUN II
Even better Resource Optimization -> Split HLT
  Idea: Buffer ALL data to disk after HLT1 / Perform Calibration & Alignment / Run HLT2 permanently in background
Farm Node
100%
For DQ only
Conditions DB
Calib&Align
Selected Events
Local disk Buffer
1 MHz
12.5 KHz
100 KHz
HLT1
HLT2
EvtBuilder

## Slide 17: Summary
LHCb Operations very successful
The strategy was good
  One operator is enough
  Integration & Homogeneity
    Allows complex feedback mechanisms
      Ex.: Re-synch or Reset a Sub-detector from Data Monitoring information
  Automated Operations
    Saves time and avoids mistakes
    But requires experience and learning…
  Further improve HLT Farm usage
    Better Trigger and Online processing closer to Offline
Related talks:
  LHCb Run I Performance: Giacomo Graziani, Monday morning
  LHCb Run II Challenges: Karol Hennessy, Friday afternoon
  LHCb Upgrades: Olaf Steinkamp, Friday afternoon
LHCb Efficiency breakdown pp collisions 2010-2012 99% channels working 99% good data for analysis